## Slide 1: Establishing Validation Acceptance Criteria on the Observed Mean and Standard Deviation for 2-Sided Dissolution Specifications Using Bayesian Methodology and Simulation
Thomas Parks, Eli Lilly & Co
Adam Rauk, Inventive Health

## Slide 2: Outline
Background on USP dissolution test <711>
Defining the problem
  Specifications on an extended release product
  Statistically supporting criteria for validation
Approaches
  ASTM E2709, “Standard Practice for Demonstrating Capability to Comply with a Lot Acceptance Procedure” (the “Bergum method)
    CuDAL (Content Uniformity and Dissolution Acceptance Limits) is validated software for calculating one-sided limits
  Bayesian approach using conjugate priors
Distributions/Model
Simulation
Results
References

## Slide 3: Background on USP <711> Dissolution Test
Purpose
  To provide in vitro drug release information
Uses
  Quality control including batch-to-batch variability
  Surrogate for in vivo testing through In Vitro/In Vivo Correlations (IVIVC)
International Conference on Harmonisation (ICH)
  The USP General Chapter <711> Dissolution test is harmonized with Europe and Japan

## Slide 4: Dissolution Setup (Apparatus 2, Paddle)

## Slide 5: Dissolution USP Test – General
USP <711> is a multi-stage test
  Stage 1: Sample 6, if fail Stage 1 criteria then
  Stage 2: Sample additional 6, if fail Stage 2 criteria then
  Stage 3: Sample additional 12 and assess against Stage 3 criteria
Total of up to 24 dosage units could be tested for a single batch
Applies to immediate release, extended release, and delayed release dosage forms

## Slide 6: USP <711> Extended Release Test

## Slide 7: Extended Release Dissolution Specs at Specified Times
T1
T2
T3
% Released

## Slide 8: Validation Criteria – FDA Guidance
FDA 2011 guidance, “Process Validation: General Principles and Practices” states,
  “The number of samples [in the process performance protocol] should be adequate to provide sufficient statistical confidence of quality…”
To provide assurance that the 2-sided dissolution specifications would be met for any other sample pulled randomly from the batch

## Slide 9: Extended Release Dissolution Specs and Acceptance Criteria
T1
T2
T3
% Released
ASTM E2709, CuDAL
???
Statistical Criteria Needed to Assure “Confidence”

## Slide 10: Problem Statement & Options
Determine acceptance criteria for 2-sided dissolution specifications to provide assurance that future dissolution results will meet the specification limits.
Options
  Implement ASTM E2709 Standard Practice for Demonstrating Capability to Comply with a Lot Acceptance Procedure
    Modify the Validated SAS program CuDAL (Content uniformity and Dissolution Acceptance Limits) to calculate 2-sided limits
  Apply an alternate approach
    A Bayesian approach with simulation

## Slide 11: ASTM E2709, Joint Confidence Region
where = probability of passing at stage i, evaluated
regardless of passing at a prior stage
Where,
And,
= probability of passing the j-th criterion of the m
criteria within the i-th stage
This results in the lower probability bound being calculated for any  and
Then, …

## Slide 12: ASTM E2709, Joint Confidence Region
A joint confidence interval can be calculated by choosing  and such that
Yields and /2
Then the joint confidence interval is,
= (1 - )

## Slide 13: ASTM E2709, Joint Confidence Region from Observed and S

## Slide 14: Bayesian 2-sided Dissolution Acceptance Criteria
Goal: Set criteria on observed mean and std dev
Approach
  Identify posterior predictive distribution (PPD) for the dissolution results
  Sample j = 1 to N times sets of n = 6, 12, 18, … dissolution results from the PPD
    Compare j-th sample to 2-sided specifications
    Determine proportion of samples that pass dissolution Stage 1 or Stage 2 criteria
  Set , S criteria based on predicted Prob(Pass)

## Slide 15: Distributions*
Let
where and j = 1 to n
Then the likelihood can be written as
For unknown  and , a conjugate prior is Normal-Gamma
* K. Murphy, “Conjugate Bayesian analysis of the Gaussian distribution”, 2007

## Slide 16: Distributions*
, where
Then the posterior can be written as
And the posterior predictive distribution is a Student’s t
* K. Murphy, “Conjugate Bayesian analysis of the Gaussian distribution”, 2007
degrees freedom, shifted mean,
,
,
, where
variance

## Slide 17: Distributions
then,
If we use a non-informative prior by setting ,
then the posterior predictive distribution is Student’s t
degrees freedom, shifted mean,
,
,
,
,
, where
variance
and,
or

## Slide 18: Simulation – Core Routine
For xbar = LSL to USL by increment1
For S = 0 to 9 by increment2
For n = 6 to 36 by 6, where n = number of dissolution results
For Sims = 1 to N
For j = 1 to n
Stage1 = LSL  tj  USL for all j
Stage2 = LSL   USL, & LSL-10  tj  USL+10 for all j
Prob(pass|xbar, S) = #pass(Stage1 or Stage2)/N

## Slide 19: Results

## Slide 20: Results

## Slide 21: Results – Combined
Over the n of interest (18-36, 3 lots), the selected polygons/acceptance regions are very similar
Accept
Reject

## Slide 22: Conclusions
Bayesian methodology provides a closed form solution for the posterior predictive distribution
Simulations from this PPD provided predictions of the probability of passing the USP <711> criteria given specified andS
The simulations provided acceptance regions for a given set of n dissolution results

## Slide 23: Comments and Questions

## Slide 24: References
http://en.wikipedia.org/wiki/Conjugate_prior
K. Murphy, “Conjugate Bayesian Analysis of the Gaussian Distribution”, 2007
United States Pharmacopeia general chapter <711>
ASTM E2709, “
M. Evans, et. al., “Statistical Distributions” 2nd ed., 1993
N. Johnson, et. al., “Continuous Univariate Distributions” vol 2, 2nd ed., 1995