## Slide 1: Some Design Recommendations For ASAP Studies
Tim Kramer, Eli Lilly and Company
Adam Rauk, Inventiv Clinical, LLC

## Slide 2: Overarching Goal
Determine temperatures, humidities and times that should be used to optimally determine shelf life (at 25°C/60% RH)
  Although degradation rate parameters are of interest, the main goal is to get a valid estimate of the shelf life

## Slide 3: Outline
Assumptions and methodology for evaluating designs
“Optimum” designs for 3, 4 and 5 environments
  Comparison with standard 5-run design
Some extensions
  Restricting designs to a subset of parameter space
  Errors in humidity and temperature in chambers
  Nonlinear degradation

## Slide 4: “Standard” 5-run Design
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 1
80 |  |  |  | 2 | 

## Slide 5: Assumptions
Degradation rate fits humidity-corrected Arrhenius equation
Degradation increases linearly with time
  Brief consideration of time0.5 or time2 dependency
True shelf life is either 2, 4 or 8 years
Activation energy is either 17.2, 25.7 or 34.3 kcal/mol

## Slide 6: Assumptions
Humidity coefficient (bRH) is 0.00, 0.04 or 0.08
Specification limit is either 0.5%, 1.0% or 2.0%
  Pre-exponential factor adjusted to achieve shelf life
Measurement uncertainty is either 6 or 10% of degradation with minimum of 0.02%

## Slide 7: Acceleration Factors
 | Activation Energy (kcals/mol) |  | 
Temperature °C | 17.2 | 25.7 | 34.3
25 | 1.0 | 1.0 | 1.0
40 | 4.0 | 8.0 | 16.0
50 | 9.5 | 28.7 | 88.2
60 | 21.1 | 95.3 | 438.2
70 | 45.0 | 295.6 | 1983.4
80 | 92.0 | 859.4 | 8242.5

## Slide 8: Equivalent Days to 4 Year Shelf Life (Linear Degradation, Arrhenius, Relative to 25°C)
 | Activation Energy (kcals/mol) |  | 
Temperature °C | 17.2 | 25.7 | 34.3
25 | 1461.0 | 1461.0 | 1461.0
40 | 363.6 | 182.9 | 91.2
50 | 154.6 | 50.9 | 16.6
60 | 69.2 | 15.3 | 3.3
70 | 32.4 | 4.9 | 0.7
80 | 15.9 | 1.7 | 0.2

## Slide 9: Allowable Design Points (Temperature and Relative Humidity)
 | % Relative Humidity |  |  |  | 
Temperature (°C) | 10 | 25 | 40 | 55 | 75
40 | X | X | X | X | X
50 | X | X | X | X | X
60 | X | X | X | X | X
70 | X | X | X | X | X
80 | X | X | X | X | X
Need to limit days of exposure to be reasonable for most combinations of assumed degradation rates

## Slide 10: Environments, Exposures and Their Expected Degradation (0.5% Spec Limit, 8 Year Shelf Life)
Bounded at 20% Increase
Only considering 1, 2, 7 or 14 day exposures

## Slide 11: Environments, Exposures and Their Expected Degradation (2.0% Spec Limit, 2 Year Shelf Life)

## Slide 12: Allowable Design Points (Temperature, Relative Humidity and Maximum Number of Days)
 | % Relative Humidity |  |  |  | 
Temperature (°C) | 10 | 25 | 40 | 55 | 75
40 | 14 | 14 | 14 | 14 | 14
50 | 14 | 14 | 14 | 14 | 14
60 | 14 | 14 | 14 | 14 | 14
70 | 14 | 14 | 14 | 7 | 2
80 | 7 | 7 | 2 | 2 | NA
Restricted combinations of temperature, humidity, and days so that ≥60 of 81 combinations of Arrhenius assumptions and shelf-life have an expected degradation increase of 5% or less or less

## Slide 13: Restricted Combinations: Environments, Exposures and Their Expected Degradation (0.5% Spec Limit, 8 Year Shelf Life)

## Slide 14: Restricted Combinations: Environments, Exposures and Their Expected Degradation (2.0% Spec Limit, 2 Year Shelf Life)

## Slide 15: Initial + 3 Condition Designs for Arrhenius, Linear in Time

## Slide 16: Simplest Search: 3 Points, Linear Degradation
Temp\RH | 10 | 25 | 40 | 55 | 75
40 | 14 |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  |  | 
70 |  |  |  |  | 2
80 | 7 |  |  |  | 
Suppose you will run samples at 3 conditions. Which conditions should you choose and how long should you store samples at each condition?
  Subject to maximum day restrictions
  Assume linear degradation
Possible Optimum

## Slide 17: Design Evaluation
Simulate data for each of 162 combinations of
  Activation Energy (3 levels)
  RH factor (3 levels)
  True shelf life (3 levels)
  Specification limit (3 levels)
  Degradation uncertainty (2 levels)
Estimate shelf life at 25°C/60% RH
Repeat n times for each combination (10 iterations initially, 100 for better designs)

## Slide 18: Design Evaluation
Bound shelf life estimate by 0.1 and 20 years
Scale estimated shelf life by true shelf life: scaled shelf life = estimated shelf life/true shelf life
  Want values near 1
Calculate squared bias: (1 – scaled shelf life)2 for each combination
Calculate average squared bias across “162 combinations times n iterations”
  Equal weight given to each combination—equal probability point prior

## Slide 19: One Iteration for One Design Proposal: Estimated Shelf Life
Orange horizontal lines represent observed averages from simulation

## Slide 20: One Iteration for One Design Proposal: Scaled Shelf Life
Orange horizontal lines represent observed averages from simulation

## Slide 21: One Iteration for One Design Proposal
Orange horizontal lines represent observed averages from simulation

## Slide 22: Optimization Routine
Generate 100 designs completely at random from the set of possible run conditions
From the top 20 designs in the total design pool, sample one. The probability of a given design being selected is proportional to 1/sqrt(mean(shelf life error)^2)
For the selected design, randomly replace one run 20 times
Generate 5 designs completely at random
Repeat steps 2-4 (200 times or more)

## Slide 23: Top 3-Run Designs: Days at Each Environment Shown
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 14
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 
80 |  |  |  | 2 | 

## Slide 24: Reminder: Possible Optimum
Temp\RH | 10 | 25 | 40 | 55 | 75
40 | 14 |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  |  | 
70 |  |  |  |  | 2
80 | 7 |  |  |  | 
Possible Optimum

## Slide 25: Theoretical Increase for “Possible Optimum”
Markers colored for each of 3 different storage environments; shapes for different humidity conditions

## Slide 26: Theoretical Increase for Found Optimum
Markers colored for each of 3 different storage environments; shapes for different humidity conditions

## Slide 27: Top 3-Run Designs: Days at Each Environment Shown
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 14
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 
80 |  |  |  | 2 | 

## Slide 28: Top 4-Run Designs: Days at Each Environment Shown
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  | 14 |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 2
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 

## Slide 29: Top 5-Run Designs: Days at Each Environment Shown
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 | 14 |  |  | 14 | 
70 |  |  |  |  | 2
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 1
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 2
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  |  | 2, 2 | 
Standard Design

## Slide 30: Possible Optimum
Temp\RH | 10 | 25 | 40 | 55 | 75
40 | 14 |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  |  | 
70 |  |  |  |  | 2
80 | 7 |  |  |  | 
Mean Squared Bias = 7.323
Bounded Parameters Mean Squared Bias = 7.523 (Restrict activation energy and relative humidity coefficients to be non-negative in non-linear fit)

## Slide 31: Top 3-Run Designs: Days at Each Environment Shown with Mean Squared Bias
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 14
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 
80 |  |  |  | 2 | 
0.475 0.263
0.324
0.321
0.295
0.307
0.299
0.313

## Slide 32: Top 4-Run Designs: Days at Each Environment Shown with Mean Squared Bias
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  | 14 |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 2
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 
0.424
0.195
0.231
0.227
0.215
0.217
0.226
0.233

## Slide 33: Top 5-Run Designs: Days at Each Environment Shown with Mean Squared Bias
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 | 14 |  |  | 14 | 
70 |  |  |  |  | 2
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  |  | 14 | 
70 | 14 |  |  |  | 1
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 2
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 14
50 |  |  |  |  | 
60 |  |  |  | 14,14 | 
70 |  |  |  |  | 
80 |  |  |  | 2, 2 | 
0.150
0.128
0.153
0.134
0.389
0.151
0.335
0.325

## Slide 34: Repeatability of Evaluations
Set (of 500 iterations x 162 Combinations) | Mean Squared Bias of Scaled Shelf Life | Square Root of Mean Squared Bias
1 | 0.1478 | 0.384
2 | 0.1494 | 0.387
3 | 0.1443 | 0.380
4 | 0.1474 | 0.384
5 | 0.1505 | 0.388
6 | 0.1521 | 0.390
7 | 0.1509 | 0.388
8 | 0.1536 | 0.392
9 | 0.1479 | 0.385
10 | 0.1513 | 0.389

## Slide 35: Other Evaluations: Limiting Range of Solutions
Ea | LH | HH
 | LL | HL
 | bRH | 
25700
17200
34300
0
0.04
0.08

## Slide 36: Top 3-Run Designs: Days at Each Environment Shown with Mean Squared Bias
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  | 2 | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 |  |  |  | 14 | 14
70 |  |  |  |  | 
80 |  |  |  | 2 | 
0.295
0.299
2 Best Designs from Full Parameter Space

## Slide 37: Top 3-Run Designs: Days at Each Environment Shown (Restricted Parameter Space)
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14
60 |  |  | 14 |  | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 14,14
60 |  |  |  |  | 2
70 |  |  |  |  | 
80 |  |  |  |  | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  | 14 | 
60 |  | 14 |  |  | 
70 |  |  |  |  | 
80 |  |  | 2 |  | 
°C\RH | 10 | 25 | 40 | 55 | 75
40 |  |  |  |  | 
50 |  |  |  |  | 
60 | 14 |  |  | 14 | 
70 |  |  |  |  | 
80 |  |  |  | 2 | 
0
0.04
0.08
17.2
25.7
34.3
?

## Slide 38: (Almost Final) Summary
Designs to optimally determine shelf life incorporate environments with appreciable degradation
  More emphasis is given to achieving appreciable degradation than spread in temperature or humidity
  Low temperatures may lead to “no information” results
  4-run designs generally incorporate anchoring of one temperature/humidity combination with 2 points and varying temperature and humidity with other two points

## Slide 39: Other Evaluations
Effect of error in humidity and temperature of environments
  Simulated with standard deviations of 1°C and 1% RH
  Optimal designs spread temperature and humidity more relative to exact environment options.
    Some emphasis on stabilizing initial condition
    More variety in the designs found that are nearly optimum
  Increases mean squared bias of shelf life estimate
    Best no noise: 0.150; Best with noise: 0.342

## Slide 40: Other Evaluations
Nonlinear response (square root of time, square of time)
  Nature of response not reliably determined from optimum 5-run design using end points alone
  Adding intermediate samples at half of maximum time allows reliable estimation of shape of response