## Slide 1: Setting Release Limits: A comparison of Frequentist and Bayesian Approaches
Niels Væver Hartvig PhD
Principal Specialist, Novo Nordisk A/S
THE 39th ANNUAL MIDWEST BIOPHARMACEUTICAL STATISTICS WORKSHOP
MAY 16–18, 2016, MUNCIE, INDIANA

## Slide 2: Definitions & Terminology
Shelf life limit (SL): Registered specification limit which the product must conform to until expiry.
Release limit (RL): Internal release limit that is used to provide confidence that a released batch complies with the shelf life limit until expiry
Shelf life (T)
All data and specification limits are constructed for illustration of principles

## Slide 3: Outline of talk: Setting internal release limits
Frequentist approach: Allen, Dukes and Gerger (1991)
Bayesian approach: Wei (1998)
Comparison of methods and recommendations
P.V. Allen, G.R. Dukes, M.E. Gerger (1991) “Determination of release limits: A General Methodology”, Pharm. Research, 8 (9)
G.C.G. Wei (1998) ”Simple methods for determination of the release limits for drug products”, J. Biopharm. Statist., 8 (1)

## Slide 4: Allen, Dukes & Gerger (1991)
Linear regression model for stability limiting parameter of actual batch:
Estimated common rate of change from historical data:
or
Estimated batch level at time T
Release batch if 95% CL is above LSL

## Slide 5: Example: Only analytical uncertainty
Number of independent results at release.
Quantile, typically ~ 1.65 for 95% confidence.
Intermediate precision of analytical method

## Slide 6: How much can we trust the release result?

## Slide 7: Release limit ensures 95% confidence
If a release result is exactly at the release limit, we have 95% confidence that the batch is within LSL throughout shelf life

## Slide 8: Impact of analytical variation
Analytical variation hurts twice:
1. Tighter release limits needed
2. More variation in release results
Target: 7.8
Process SD = 0.05

## Slide 9: Example: Stability degradation
Estimated degradation during shelf life
Uncertainty of estimated degradation

## Slide 10: Degradation rate estimated from historical data
b is the common degradation rate for all batches.
Degradation rates for different batches cannot be different!

## Slide 11: What if batches are not similar?
Mixed model with random slope:

## Slide 12: Extension to random batch-slope
Batch-slope variance

## Slide 13: Examples of variation between batches
Batch-to-batch variation narrows release limits

## Slide 14: Combined specifications: DS & DP
DS internal release limit (combined confidence)
DS degradation during storage and formulation
Uncertainty of DS degradation
Internal release limit for DS ensures with high confidence that DP will comply with USL, but not that DP will comply with internal release limit!

## Slide 15: Separate confidence for each test instance
Statistical confidence for each test instance narrows release limits

## Slide 16: Wei (1998)
Release and stability data on actual batch:
Historical data:
or
Least-squares estimate of batch level based on data available at time T
Conditional distribution used for release:
*A conditional least-squares estimate is used in the paper

## Slide 17: Wei’s release limit depends on test plan for batch
To compare the two approaches, we consider the Wei method assuming only release data for a batch.
ADG
Release data
Wei
Release and future stability data

## Slide 18: Wei’s two principles
Conditional limits (ADG’s principle)
  Conditionally on a release result from a batch, ensures that this batch remains within spec with high confidence, based only on historical stability estimate and the release result.
Unconditional limits
  Ensures that for the population of batches as a whole we will have low risk of OOS, by combining the knowledge obtained from the release result with the assumption that the process has only been subject to normal random variation.

## Slide 19: Predicted mean at EOS based on release data
Conditional principle (ADG):
Unconditional principle:

## Slide 20: Illustration of P(μiT|Yi0)
Conditional principle (ADG):
Unconditional principle:
The following slides illustrate the difference in the distribution P(μiT|Yi0) in the conditional principle and unconditional principle

## Slide 21: Illustration of P(μiT|Yi0)
The unconditional method uses the normal distribution of the manufacturing process to bias the mean towards the historical mean

## Slide 22: Illustration of P(μiT|Yi0)
When the release result is at the ADG-release limit there is 5% chance that the mean is outside LSL at time T in the conditional method.
In the unconditional method, the risk is much lower.

## Slide 23: Illustration of P(μiT|Yi0)
When the risk in the unconditional density is 5%, the conditional density is much higher – here 50%.

## Slide 24: Illustration of P(μiT|Yi0)
When the measurement uncertainty is high, the conditional method is more conservative and the unconditional even more biased towards the historical mean.

## Slide 25: Illustration of P(μiT|Yi0)
Even when the risk is 50% for the conditional method, the risk is virtually 0 for the unconditional.

## Slide 26: Illustration of P(μiT|Yi0)
When measurement error is low – the two distributions are very similar.

## Slide 27: Illustration of risk controlled
Conditional principle (ADG):
Unconditional principle:
The following slide illustrates the difference in the risk controlled by the two methods

## Slide 28: Risk controlled by the methods
The unconditional method controls the overall risk of OOS for the population.
The conditional method controls the risk of OOS for each single batch

## Slide 29: The use of the two methods are quite different
Conditional (ADG) | Unconditional (Wei)
Each batch is evaluated based on the release result | Batches are evaluated based on the release result AND the assumption that the process is in statistical control
In principle the release limit alone protects us against OOS at stability. SPC of the manufacturing process is for preventive reaction and not a prerequisite for releasing a batch. | The assumption that the process is in statistical control is central and this should be verified by careful use of statistical control charts, short-term review of incidents etc. before releasing the batch
The higher the analytical uncertainty, the more conservative is the ADG approach – and the worse is the process capability | The higher the analytical uncertainty, the more critical is the assumption that the process is in control
Can be used to assess the risk for isolated batches | Cannot be used to evaluate isolated batches

## Slide 30: Conclusions: Internal release limits
The frequentist (or conditional) method provides confidence for each single batch based on release data only. This may result in narrow internal release limits, for instance when analytical uncertainty is high.
The unconditional Bayesian principle provides much wider internal release limits, but at the price of specific assumptions:
  The manufacturing process must be in statistical control with known mean and standard deviation
  Only the overall of risk of OOS is controlled, not the OOS risk for each individual batch